## Slide 1
Fall Management
New Product Release
Notes: 1
DY

## Slide 2: Agenda
  Direct Connect Cordless Monitor
  CSM-BC500
  Motion Sensor
  CS-MS100
  Door Wander System
  WM-KIT1
PRODUCT Training

## Slide 3: Cordless Direct Connect Monitor (CSM-BC500)
CSM-BC500 Direct Connect Monitor

## Slide 4: Cordless Direct Connect Monitor (CSM-BC500)
Simple, low cost cordless bed and chair monitor
  Alternative solution to BC400 or BC201
Eliminates cord tripping hazards and cord damage when used with cordless sensors.
Battery and pad replacement notification
Silent alarm, reduce alarm fatigue.
  No audible alarm from monitor
Plugs directly into nurse call.
  Activates an audible alarm through nurse call
CSM-BC500 Direct Connect Monitor
Notes: Handout DFU and Product info sheet

## Slide 5: Cordless Direct Connect Monitor (CSM-BC500)
Open the battery compartment:
Install Three “AAA” Batteries
Close cover and secure screw
Optional: Add AC Adaptor (5v/500mA) to extend Battery Life
SETTING UP MONITOR

## Slide 6: Cordless Direct Connect Monitor (CSM-BC500)
SETTING UP MONITOR
Call Cord switch is to be in the “OFF” position if not using a call cord and before initially inserting the nurse call plug or cable into the patient station
If using with the Call Cord, switch to “ON” after connected to the patient station and inserting the Call Cord

## Slide 7: Cordless Direct Connect Monitor (CSM-BC500)
SETTING UP MONITOR
The monitor is factory set to be non-latching (compatible with industry-standard latching nurse call systems).
To change the monitor to latching, press and hold the program button for approximately 15 seconds until both LEDs flash simultaneously three times.
Notes: The monitor is intended only to be connected to a nurse call system, so that when the alarm is activated, a call will be placed to the nurse’s station. The monitor is compatible with a normally open nurse call system only, using a 1⁄4" mono nurse call jack.

## Slide 8: Cordless Direct Connect Monitor (CSM-BC500)
SETTING UP MONITOR
To change back from latching to non-latching, press and hold the program button for approximately 15 seconds until both LEDs flash simultaneously two times.

## Slide 9: Cordless Direct Connect Monitor (CSM-BC500)
Compatible with up to THREE Sensor Pads
  2 WIRELESS sensor pads
    Up to 30 ft. cordless range
  1 CORDED sensor pads
USING MULTIPLE SENSORS

## Slide 10: Cordless Direct Connect Monitor (CSM-BC500)
Press and hold the black programming button located on the bottom of the monitor for approximately 3 seconds
Both yellow and green LED’s will then light for 15 seconds
SYNCHRONIZING WITH CORDLESS SENSOR

## Slide 11: Cordless Direct Connect Monitor (CSM-BC500)
Within 10 seconds, place pressure on the sensor pad and then release.
The yellow LED will then blink once, confirming the monitor and pad are now synchronized and ready for use.
SYNCHRONIZING WITH CORDLESS SENSOR

## Slide 12: Cordless Direct Connect Monitor (CSM-BC500)
UNSYNCHRONIZING WITH CORDLESS SENSOR
Press and hold the PROGRAM button first, then press and hold the RESET button at the same time, for two seconds
The yellow and green LED’s will simultaneously flash three times indicating that the pad(s) has been unsynchronized

## Slide 13: Cordless Direct Connect Monitor (CSM-BC500)
Plug the sensor cord into the monitor’s sensor jack
Both LEDs flash 3 times simultaneously
CORDED SENSOR USE

## Slide 14: Cordless Direct Connect Monitor (CSM-BC500)
Connects directly into nurse call
Option to side mount with nurse call cord connection
  BC500 wall-mount bracket is available and sold separately
  Adaptor sold separately
  Velcro attachment is not recommended – If call cord used, risk of detaching
INSERT INTO patient station

## Slide 15: Cordless Direct Connect Monitor (CSM-BC500)
The RESET button provides the following two functions
  Cancels the alarm
  Places the monitor into a pause mode
USING THE MONITOR:

## Slide 16: Cordless Direct Connect Monitor (CSM-BC500)
USING THE MONITOR:
Testing the alarm
  When pressure is placed back on the pad, the GREEN LED will blink two times and then continuously every three seconds indicating the pad is in use

## Slide 17: Cordless Direct Connect Monitor (CSM-BC500)
USING THE MONITOR:
Testing the alarm
  Remove pressure from the pad to activate the alarm
  The Red LED will then blink (for 10 seconds)
  An audible alarm will only occur from the Nurse Call System in the room and patient station or just at the patient station (depending on nurse call station)

## Slide 18: Cordless Direct Connect Monitor (CSM-BC500)
USING THE MONITOR:
Testing the alarm
  To cancel the alarm, press the monitors RESET button and CANCEL the nurse call alarm at the patient station

## Slide 19: Cordless Direct Connect Monitor (CSM-BC500)
Using the PAUSE MODE
  While patient is on the pad, press the RESET button on the top of the monitor
  The patient may be removed from pad within 30 seconds without activating an alarm
  The monitor will then stay in the pause mode for the full 30 seconds and reactivate once the patient is put back on the pad
USING THE MONITOR:
1
2
3

## Slide 20: LED Indicators:
Direct Connect Cordless Monitor (CSM-BC500)
LED status located on the battery compartment side
Cordless Direct Connect Monitor (CSM-BC500)
LED STATUS:

## Slide 21: LED Indicators:
Direct Connect Cordless Monitor (CSM-BC500)
Green LED is continuously blinking
Monitoring
Cordless Direct Connect Monitor (CSM-BC500)
LED STATUS:

## Slide 22: Cordless Direct Connect Monitor (CSM-BC500)
Direct Connect Cordless Monitor (CSM-BC500)
Red LED is continuously blinking
Alarming
LED STATUS:

## Slide 23: LED Indicators:
Direct Connect Cordless Monitor (CSM-BC500)
Yellow LED is continuously blinking
Low Battery
Cordless Direct Connect Monitor (CSM-BC500)
LED STATUS:

## Slide 24: Cordless Direct Connect Monitor (CSM-BC500)
Direct Connect Cordless Monitor (CSM-BC500)
Yellow LED flashes twice continuously
Corded Pad Disconnected
1…
2…
LED STATUS:

## Slide 25: Cordless Direct Connect Monitor (CSM-BC500)
Direct Connect Cordless Monitor (CSM-BC500)
Red LED flashes twice continuously
Cordless Pad Signal Lost
1…
2…
LED STATUS:

## Slide 26: LED Indicators:
Direct Connect Cordless Monitor (CSM-BC500)
Red LED flashes three times continuously
Replace Curbell Pad
1…
2…
3
Cordless Direct Connect Monitor (CSM-BC500)
LED STATUS:

## Slide 27: Cordless Direct Connect Monitor (CSM-BC500)
Dimensions 3"H x 1.75"W x 1.75"D
Frequency: UHF - 433.92MHz+/-0.5
Battery operated
  Three AAA (included)
    ~3-4 months lifespan
  Optional AC Adaptor (sold separately)
    Length 72” (182cm)
    Extends battery life
      ~1 year
CSM-BC500 SPECS

## Slide 28: Cordless Direct Connect Monitor (CSM-BC500)
Compatible with non-latching and latching nurse call systems
ETL, FCC
Two year warranty
MSRP $139.95
  CSM-BC201 $124.95
  CSM-BC400 $208.95
ADDITIONAL INFO:
CSM-BC500 Information Sheet

## Slide 29: Cordless Direct Connect Monitor (CSM-BC500)
Easy to use, low cost cordless monitor option when compared to BC400
Where not having an in-room audible alarm is a concern
  Noise Reduction
  Patient Satisfaction
Where 3 sensors may be needed
  2 Cordless, 1 Corded
Need a latching monitor for system compatibility
  Field Programmable
Suggested Applications

## Slide 30
Question/Answer

## Slide 31: Motion Sensor (CS-MS100)
CS-MS100 Motion Sensor

## Slide 32: Motion Sensor (CS-MS100)
Simple, low cost motion detection solution
  Ideal alternative for low risk patient monitoring
Small, compact design that can mount anywhere
  Can be installed horizontally or vertically on most surfaces
Infrared motion detection works in light and dark conditions
  Great for detecting patients’ movement at nighttime – reducing fall risk
CS-MS100 Motion Sensor
Notes: Handout DFU and Product info sheet

## Slide 33: Motion Sensor (CS-MS100)
Infrared motion detection
60º detection angle
180º adjustable mounting bracket
Built-in Speaker
CS-MS100 Features
Notes: Handout DFU and Product info sheet

## Slide 34: Motion Sensor (CS-MS100)
Rotate the sensor in the bracket to access the battery door
Slide open the battery door cover located on the back
Connect the 9-volt battery and wait 60 seconds before use
Replace the battery door cover
SETTING UP THE SENSOR ALARM

## Slide 35: Motion Sensor (CS-MS100)
SENSOR MODES
  Alarm Mode
    When motion is detected, audible alarm for 15 seconds and then stops
    Remains silent until it detects motion again
  Chime Mode
    When motion is detected, monitor will chime twice and then stops
    Remains silent until it detects motion again
SETTING UP THE SENSOR ALARM

## Slide 36: Motion Sensor (CS-MS100)
INSTALLING THE SENSOR ALARM
Determine the desired area to be monitored
  Stand Alone - Local alarm only, does not integrate with Nurse Call
Can be installed horizontally or vertical

## Slide 37: Motion Sensor (CS-MS100)
Compact Size
  4" H x 2.5” W x 1.25”
Wall-mounted bracket
  Screws and foam tape (included)
Battery operated
  One 9-volt battery (included)
CS-MS100 Specs

## Slide 38: Motion Sensor (CS-MS100)
One year warranty
MSRP $37.90
ADDITIONAL INFO:
CS-MS100 Information Sheet

## Slide 39: Motion Sensor Applications
Simple low cost monitoring alternative to bed, chair and floor sensor pad technology
Ideal application when nurse call connectivity is not needed
Chime mode at room entrances to help with wandering residents and privacy concerns
Suggested Applications

## Slide 40
Question/Answer

## Slide 41: Door Wander System (WM-KIT1)
WM-KIT1 Wander Management System

## Slide 42: Door Wander System (WM-KIT1)
Simple solution to help prevent patients from wandering off the premises
Low cost alternative to more complex, very expensive wander management systems
Flexibility of the system allows you to customize to your facility’s needs
  Monitoring many patients at one time in a common area
  Monitoring one patient in a single room
WM-KIT1 Wander Management System
Notes: Handout DFU and Product info sheet

## Slide 43: Door Wander System (WM-KIT1)
Wristband wearer sets off alarm when in range of Door Strip Sensor
Alarm cancelled by pressing Reset Button at wall
Stand alone
  Local alarm only, does not integrate with Nurse Call
Included magnetic door contact can be used so that the alarm sounds when door is opened
WM-KIT1 Features and Benefits
Notes: AC Adapter cord is 54” (137cm)
Handout DFU and Product info sheet

## Slide 44: Door Wander System (WM-KIT1)
WM-KIT1 COMPONENTS
Wristband
Door Strip Sensor
AC Adaptor
Wall-Mounted
Reset Button
Notes: AC Adapter cord is 54” (137cm)

## Slide 45: Door Wander System (WM-KIT1)
Mount the door strip sensor next to the door, and plug it into an AC outlet
Foam adhesive mount (included) not to be screwed in
Audible and visual LED red light alarm when triggered
Door Strip Sensor

## Slide 46: Door Wander System (WM-KIT1)
On the door strip sensor remove the cap on the opposite end as the AC adapter
  Make sure AC adapter is unplugged before removing cap
Adjusting Volume
The volume control is the small blue potentiometer
Adjust using a small screwdriver. Counter clock-wise to INCREASE the volume and clockwise to DECREASE to silent

## Slide 47: Door Wander System (WM-KIT1)
Adjusting detection range
The Detection Range Control is the labeled 0 (longest range) – F (shortest range)
Adjust using a small screwdriver. Counter clock-wise to INCREASE the range and clockwise to DECREASE to range
  Adjustable up to 26’
On the door strip sensor remove the cap on the opposite end as the AC adapter
  Make sure AC adapter is unplugged before removing cap

## Slide 48: Door Wander System (WM-KIT1)
Magnetic Door Contact(optional use)
Includes Magnetic Door Contact
  Optional ability to trigger alarm only when a wristband transmitter is within range and the door is opened
  The contacts must be within 1” on each other when the door is closed

## Slide 49: Door Wander System (WM-KIT1)
On the door strip sensor remove the cap on the same end as the AC adapter
  Make sure AC adapter is unplugged before removing cap
Locate 0V and Contact inputs on the blue connector.
Connect supplied magnetic door contact
  There is no determination of polarity on the cable
    Either wire of the cable can be connected to the “0V” or “Contact” inputs
Connecting to door sensor

## Slide 50: Door Wander System (WM-KIT1)
  Reset Button cancels the alarm
  Battery operated
  ~ 3 year life span - Entire unit replaced when battery has died
  If Reset Button is pressed and the Red LED is dimly lit or does not come on, the battery is low or dead
  Mounts on wall (screws/sleeves included) within 15' from the door strip sensor
  Alarm may also be canceled by placing the magnetic programming key fob over the blue dot on the side of the door strip monitor
WALL-Mount reset button

## Slide 51: Door Wander System (WM-KIT1)
Worn on the patient wrist
  Triggers the alarm when within range of the door strip monitor
Reusable, watchband-style bands
  Two included with kit
Wristband Transmitter
  Single patient use wristbands (WM-SUWB-10PK) may be ordered separately

## Slide 52: Door Wander System (WM-KIT1)
Activating the wristband transmitter
  Place the magnetic key fob next to the button, opposite the end with the LED.
  The LED will flash three times to indicate it has successfully been activated
Wristband Transmitter
Wristband transmitter is battery operated
  ~ 3 year life span
  Entire unit replaced when battery has died

## Slide 53: Door Wander System (WM-KIT1)
AC Power: Class 2 AC Adaptor
  Output DC 12V 300 mA
  AC Adapter cord length is 54” (137cm)
  Dimensions
  Door strip Sensor
    32.56" L x 1.43" W x .75" D
  Reset Button
    3.375" H x 3.375" W x .4375" D
Frequency: UHF - 433.92MHz+/-0.5
Detection range adjustable up to 26'
WM-KIT1 SPECS

## Slide 54: Door Wander System (WM-KIT1)
All components may be ordered individually to customize to facility needs
One year warranty
MSRP $843.25
ADDITIONAL INFO:
WM-KIT1 Information Sheet

## Slide 55: Door Wander System (WM-KIT1)
Simple, low cost solution to help control patient wandering
Assisted Living, Independent Living, LTC facilities
  Memory Care units
  Dementia Units
Requires facility and/or maintenance assistance with installation
  Licensed electrician may also be needed to provide power
Suggested Applications

## Slide 56: Door Wander System (WM-KIT1)
High end/high cost wandering and tracking system manufactures and installers (examples):
  Stanley / WanderGuard
  SecureCare
  Accutech
RTLS technology/products
  Automatically identify and track the location of objects or people in real time, usually within a building or other contained area
Door lock and keypad door access control products
Competition

## Slide 57
Question/Answer
Notes: 57

## Slide 58
Thank you
Notes: 58